------------------------------------------------------------------------------

  traKmeter
  =========
  Loudness meter for correctly setting up tracking and mixing levels

  Copyright (c) 2012-2015 Martin Zuther (http://www.mzuther.de/)

  This program is free software: you can redistribute it and/or modify
  it under the terms of the GNU General Public License as published by
  the Free Software Foundation, either version 3 of the License, or
  (at your option) any later version.

  This program is distributed in the hope that it will be useful,
  but WITHOUT ANY WARRANTY; without even the implied warranty of
  MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
  GNU General Public License for more details.

  You should have received a copy of the GNU General Public License
  along with this program. If not, see <http://www.gnu.org/licenses/>.

  Thank you for using free software!

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit, stereo)
====================================================
Please verify correctness of signal meters visually.

00:00.000 - 00:02.000 silence
00:02.000 - 00:05.000 sine wave (997 Hz)

        [left channel: -60.10 dB FS peak]
        [right channel: -59.90 dB FS peak]

        [left signal meter should not light]
        [right signal meter should light]

00:05.000 - 00:07.000 silence
00:07.000 - 00:17.000 sine wave (997 Hz, volume sweep)

        [left channel: -60.10 dB FS to -20.10 dB FS peak]
        [right channel: -19.90 dB FS to -59.90 dB FS peak]

        [left signal meter should light]
        [right signal meter should light]

00:17.000 - 00:19.000 silence
00:19.000 - 00:19.100 sine wave burst (997 Hz)

        [left channel: -0.10 dB FS peak]
        [right channel: +0.00 dB FS peak, clipped waveform]

        [left signal meter should light]
        [right signal meter should light]

00:19.100 - 00:21.100 silence

Validation settings
===================
File: signal_meters_stereo.flac
Host SR: 44 100 Hz
Channel: All
Display: [ ] Peak meter level
        [ ] Average meter level