------------------------------------------------------------------------------

  This documentation and its accompanying audio file by Martin Zuther is
  licensed under a Creative Commons Attribution-ShareAlike 4.0 International
  License.

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 24 bit, stereo)
====================================================
Please verify correctness of peak and average meters programmatically and visually.

Given levels describe the left channel, while the right channel has been amplified by +0.20 dB. All readouts should be validated on both peak and average meters.

00:00.000 - 00:01.000 silence
00:01.000 - 00:04.000 sine wave (997 Hz, -24.1 dB FS peak)

        [left level meters should read -24.1 dB]
        [right level meters should read -23.9 dB]

00:04.000 - 00:05.000 silence
00:05.000 - 00:08.000 sine wave (997 Hz, -23.1 dB FS peak)

        [left level meters should read -23.1 dB]
        [right level meters should read -22.9 dB]

00:08.000 - 00:09.000 silence
00:09.000 - 00:12.000 sine wave (997 Hz, -22.1 dB FS peak)

        [left level meters should read -22.1 dB]
        [right level meters should read -21.9 dB]

00:12.000 - 00:13.000 silence
00:13.000 - 00:16.000 sine wave (997 Hz, -21.1 dB FS peak)

        [left level meters should read -21.1 dB]
        [right level meters should read -20.9 dB]

00:16.000 - 00:17.000 silence
00:17.000 - 00:20.000 sine wave (997 Hz, -20.1 dB FS peak)

        [left level meters should read -20.1 dB]
        [right level meters should read -19.9 dB]

00:20.000 - 00:21.000 silence
00:21.000 - 00:24.000 sine wave (997 Hz, -19.1 dB FS peak)

        [left level meters should read -19.1 dB]
        [right level meters should read -18.9 dB]

00:24.000 - 00:25.000 silence
00:25.000 - 00:28.000 sine wave (997 Hz, -18.1 dB FS peak)

        [left level meters should read -18.1 dB]
        [right level meters should read -17.9 dB]
00:28.000 - 00:29.000 silence
00:29.000 - 00:32.000 sine wave (997 Hz, -17.1 dB FS peak)

        [left level meters should read -17.1 dB]
        [right level meters should read -16.9 dB]

00:32.000 - 00:33.000 silence
00:33.000 - 00:36.000 sine wave (997 Hz, -16.1 dB FS peak)

        [left level meters should read -16.1 dB]
        [right level meters should read -15.9 dB]

00:36.000 - 00:37.000 silence
00:37.000 - 00:40.000 sine wave (997 Hz, -15.1 dB FS peak)

        [left level meters should read -15.1 dB]
        [right level meters should read -14.9 dB]

00:40.000 - 00:41.000 silence
00:41.000 - 00:44.000 sine wave (997 Hz, -14.1 dB FS peak)

        [left level meters should read -14.1 dB]
        [right level meters should read -13.9 dB]

00:44.000 - 00:45.000 silence
00:45.000 - 00:48.000 sine wave (997 Hz, -13.1 dB FS peak)

        [left level meters should read -13.1 dB]
        [right level meters should read -12.9 dB]

00:48.000 - 00:49.000 silence
00:49.000 - 00:52.000 sine wave (997 Hz, -12.1 dB FS peak)

        [left level meters should read -12.1 dB]
        [right level meters should read -11.9 dB]

00:52.000 - 00:53.000 silence
00:53.000 - 00:56.000 sine wave (997 Hz, -11.1 dB FS peak)

        [left level meters should read -11.1 dB]
        [right level meters should read -10.9 dB]

00:56.000 - 00:57.000 silence
00:57.000 - 01:00.000 sine wave (997 Hz, -10.1 dB FS peak)

        [left level meters should read -10.1 dB]
        [right level meters should read -9.9 dB]

01:00.000 - 01:01.000 silence
01:01.000 - 01:04.000 sine wave (997 Hz, -9.1 dB FS peak)

        [left level meters should read -9.1 dB]
        [right level meters should read -8.9 dB]

        [left overload meter should be empty]
        [right overload meter should read -9]

01:04.000 - 01:05.000 silence
01:05.000 - 01:08.000 sine wave (997 Hz, -8.1 dB FS peak)

        [left level meters should read -8.1 dB]
        [right level meters should read -7.9 dB]

        [left overload meter should read -8]
        [right overload meter should read -8]

01:08.000 - 01:09.000 silence
01:09.000 - 01:12.000 sine wave (997 Hz, -0.1 dB FS peak)

        [left average meter should read -0.1 dB]
        [right average meter should read +0.1 dB]
        [left peak meter should read -0.1 dB]
        [right peak meter should read +0.0 dB]

        [left overload meter should read 0]
        [right overload meter should read 0]

01:12.000 - 01:13.000 silence

Validation settings
===================
File: level_meters_stereo.flac
Host SR: 44 100 Hz
Channel: All
Display: [x] Peak meter level
        [x] Average meter level