------------------------------------------------------------------------------

  This documentation and its accompanying audio file by Martin Zuther is
  licensed under a Creative Commons Attribution-ShareAlike 4.0 International
  License.

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 16 bit, 8 channels)
========================================================
Please verify correctness of peak and average meters visually.

Given levels describe the first channel. The other channels have been amplified in steps of +5.00 dB per channel (first test) and +1.00 dB (all other tests), respectively.

00:00.000 - 00:01.000 silence
00:01.000 - 00:04.000 sine wave (997 Hz, -60.10 dB FS peak)

        [signal meter ch. 1 should not light]
        [signal meter ch. 2 should light]
        [signal meter ch. 3 should light]
        [signal meter ch. 4 should light]
        [signal meter ch. 5 should light]
        [signal meter ch. 6 should light]
        [signal meter ch. 7 should light]
        [signal meter ch. 8 should light]

00:04.000 - 00:05.000 silence
00:05.000 - 00:08.000 sine wave (997 Hz, -24.05 dB FS peak)

        [peak meter ch. 1 should read -24.05 dB]
        [peak meter ch. 2 should read -23.05 dB]
        [peak meter ch. 3 should read -22.05 dB]
        [peak meter ch. 4 should read -21.05 dB]
        [peak meter ch. 5 should read -20.05 dB]
        [peak meter ch. 6 should read -19.05 dB]
        [peak meter ch. 7 should read -18.05 dB]
        [peak meter ch. 8 should read -17.05 dB]

        [RMS meter ch. 1 should read -24.05 dB]
        [RMS meter ch. 2 should read -23.05 dB]
        [RMS meter ch. 3 should read -22.05 dB]
        [RMS meter ch. 4 should read -21.05 dB]
        [RMS meter ch. 5 should read -20.05 dB]
        [RMS meter ch. 6 should read -19.05 dB]
        [RMS meter ch. 7 should read -18.05 dB]
        [RMS meter ch. 8 should read -17.05 dB]

        [maximum peaks should not be visible]
        [all signal meters should light]

00:08.000 - 00:08.500 silence
00:08.500 - 00:11.500 sine wave (997 Hz, -23.95 dB FS peak)

        [peak meter ch. 1 should read -23.95 dB]
        [peak meter ch. 2 should read -22.95 dB]
        [peak meter ch. 3 should read -21.95 dB]
        [peak meter ch. 4 should read -20.95 dB]
        [peak meter ch. 5 should read -19.95 dB]
        [peak meter ch. 6 should read -18.95 dB]
        [peak meter ch. 7 should read -17.95 dB]
        [peak meter ch. 8 should read -16.95 dB]

        [RMS meter ch. 1 should read -23.95 dB]
        [RMS meter ch. 2 should read -22.95 dB]
        [RMS meter ch. 3 should read -21.95 dB]
        [RMS meter ch. 4 should read -20.95 dB]
        [RMS meter ch. 5 should read -19.95 dB]
        [RMS meter ch. 6 should read -18.95 dB]
        [RMS meter ch. 7 should read -17.95 dB]
        [RMS meter ch. 8 should read -16.95 dB]

        [maximum peaks should be visible]
        [all signal meters should light]

00:11.500 - 00:12.500 silence
00:12.500 - 00:15.500 sine wave (997 Hz, -16.05 dB FS peak)

        [peak meter ch. 1 should read -16.05 dB]
        [peak meter ch. 2 should read -15.05 dB]
        [peak meter ch. 3 should read -14.05 dB]
        [peak meter ch. 4 should read -13.05 dB]
        [peak meter ch. 5 should read -12.05 dB]
        [peak meter ch. 6 should read -11.05 dB]
        [peak meter ch. 7 should read -10.05 dB]
        [peak meter ch. 8 should read -9.05 dB]

        [RMS meter ch. 1 should read -16.05 dB]
        [RMS meter ch. 2 should read -15.05 dB]
        [RMS meter ch. 3 should read -14.05 dB]
        [RMS meter ch. 4 should read -13.05 dB]
        [RMS meter ch. 5 should read -12.05 dB]
        [RMS meter ch. 6 should read -11.05 dB]
        [RMS meter ch. 7 should read -10.05 dB]
        [RMS meter ch. 8 should read -9.05 dB]

        [maximum peaks should not be visible]
        [all signal meters should light]

00:15.500 - 00:16.000 silence
00:16.000 - 00:19.000 sine wave (997 Hz, -15.95 dB FS peak)

        [peak meter ch. 1 should read -15.95 dB]
        [peak meter ch. 2 should read -14.95 dB]
        [peak meter ch. 3 should read -13.95 dB]
        [peak meter ch. 4 should read -12.95 dB]
        [peak meter ch. 5 should read -11.95 dB]
        [peak meter ch. 6 should read -10.95 dB]
        [peak meter ch. 7 should read -9.95 dB]
        [peak meter ch. 8 should read -8.95 dB]

        [RMS meter ch. 1 should read -15.95 dB]
        [RMS meter ch. 2 should read -14.95 dB]
        [RMS meter ch. 3 should read -13.95 dB]
        [RMS meter ch. 4 should read -12.95 dB]
        [RMS meter ch. 5 should read -11.95 dB]
        [RMS meter ch. 6 should read -10.95 dB]
        [RMS meter ch. 7 should read -9.95 dB]
        [RMS meter ch. 8 should read -8.95 dB]

        [maximum peaks should be visible]
        [all signal meters should light]

00:19.000 - 00:20.000 silence

Validation settings
===================
File: level_meters_multi.flac
Host SR: 44 100 Hz
Channel: All
Display: [ ] Peak meter level
        [ ] Average meter level