------------------------------------------------------------------------------

  This documentation and its accompanying audio file by Martin Zuther is
  licensed under a Creative Commons Attribution-ShareAlike 4.0 International
  License.

------------------------------------------------------------------------------

FLAC-compressed wave file (44.1 kHz, 24 bit, stereo)
====================================================
Please verify correctness of signal meters visually.

00:00.000 - 00:02.000 silence
00:02.000 - 00:05.000 sine wave (997 Hz)

        [left channel: -60.10 dB FS peak]
        [right channel: -59.90 dB FS peak]

        [left signal meter should not light]
        [right signal meter should light]

00:05.000 - 00:07.000 silence
00:07.000 - 00:17.000 sine wave (997 Hz, volume sweep)

        [left channel: -60.10 dB FS to -20.10 dB FS peak]
        [right channel: -19.90 dB FS to -59.90 dB FS peak]

        [left signal meter should light]
        [right signal meter should light]

00:17.000 - 00:19.000 silence
00:19.000 - 00:19.100 sine wave burst (997 Hz)

        [left channel: -0.10 dB FS peak]
        [right channel: +0.00 dB FS peak, clipped waveform]

        [left signal meter should light]
        [right signal meter should light]

00:19.100 - 00:21.100 silence

Validation settings
===================
File: signal_meters_stereo.flac
Host SR: 44 100 Hz
Channel: All
Display: [ ] Peak meter level
        [ ] Average meter level